## Slide 1: Observation operators for assimilation of satellite observations in river inundation forecasting
  1 Department of Meteorology, University of Reading, UK
  2 Department of Mathematics and Statistics, University of Reading, UK
  3 MARUM Center for Marine Environmental Sciences and Department of Geosciences,
  University of Bremen, Germany
Acknowledgements:
The authors gratefully acknowledge the NERC SCENARIO studentship supporting Elizabeth Cooper, and CASE sponsorship from the Satellite Applications Catapult.
This work was also supported in part by NERC grants NE/K00896X/1 and NE/K008900/1 as well as EPSRC grant EP/P002331/1.
Elizabeth Cooper1, Sarah Dance1,2, Javier Garcia-Pintado3, Nancy Nichols1,2, Polly Smith2.

## Slide 2: Inundation Forecasting
Inflow (m3/s)
Time (h)
Uncertainty in inputs leads to uncertainty in inundation forecast.
Topographical information e.g. (DTM)
Shallow water equations with good parameter values
e.g. channel friction parameter

## Slide 3: Observations from synthetic aperture radar (SAR)
TerraSar-X image taken from Mason et al. doi:10.1016/j.rse.2012.06.017
© DLR 2007
Light areas are dry (rough surface, higher backscatter values)
Dark areas are wet (smooth surfaces, lower backscatter values

## Slide 4: Data assimilation: ensemble transform Kalman filter
Ensemble transform Kalman filter (ETKF) approach.
Mean and perturbations updated separately.
Observation operator, H, maps state vector into observation space.
Update equation:
Innovation, d
Mean forecast observation equivalent

## Slide 5: Using observations from SAR in DA
Ensemble of i= 1,N state vectors

## Slide 6: Flood edge WLOs from SAR water level observations
1.Observation
At flood edge, water elevation = terrain elevation
2. H [x]
Extracts elevation at observation position from each ensemble member

## Slide 7: Water level observations
Observation
Mean forecast observation
innovation
Simple assimilation of the water elevation at the flood edge works well when the forecast is deeper than the truth…...

## Slide 8: Water level observations
…. but not when the forecast is shallower than the truth…..
Innovation = zero
Observation = mean forecast observation

## Slide 9: Water level observations
…. unless we use a ‘nearest wet pixel’ approach.
innovation
Not easy to locate ‘nearest wet pixel’ in practise
Observation
Mean forecast observation

## Slide 10: Nearest wet pixel
X
X

## Slide 11: New approach: backscatter observations
Fit two Gaussian curves to give mean and variance of wet and dry pixel distributions
H(x): assign value of md to pixel if forecast predicts dry; mw if model predicts wet
Wet pixels
Dry pixels
mw
md
As per : L. Giustarini et al., "Probabilistic Flood Mapping Using Synthetic Aperture Radar Data," in IEEE Trans on Geoscience and Remote Sensing,Dec. 2016.
OBSERVATION: measured backscatter value in chosen pixels

## Slide 12
Methodology
Twin experiments in idealised topography
  3 observation operator approaches
  Noisy synthetic observations from `truth’
  12 hourly intervals
  3 observation positions
12
Ensemble forecast system with 100 members
Inflows and channel friction parameter perturbed

## Slide 13: Results: state estimation
Channel friction parameter too HIGH: forecast water levels too DEEP
CONCLUSION: all of the operators do a good job at assimilation times

## Slide 14: Results: state estimation
Channel friction parameter too LOW: forecast water levels too SHALLOW
CONCLUSION:
simple flood edge operator does a bad job (as expected)
nearest wet pixel operator slightly better than backscatter operator

## Slide 15: Results: Joint state-parameter estimation
Channel friction parameter too HIGH: forecast water levels too DEEP
CONCLUSION: All operators improve the forecast relative to open loop.

## Slide 16: Results: Joint state-parameter estimation
Channel friction parameter too LOW: forecast water levels too SHALLOW
CONCLUSION: Simple operator does not work
Backscatter operator shows potential

## Slide 17: Conclusions
Our experiments have shown:
    Choice of observation operator is REALLY IMPORTANT!
    `Nearest wet pixel’ in these experiments works well…. but best case scenario as no complicated terrain
    Our novel approach using backscatter observations is promising
      Can use more observations from all of domain
      No terrain complications: may be cheaper
    Further experiments required to determine
      how operators compare in operation (real SAR and topography)
      how many observations can we use?

## Slide 18: Conclusions
Our experiments have shown:
    Choice of observation operator is REALLY IMPORTANT!
    `Nearest wet pixel’ in these experiments works well…. but best case scenario as no complicated terrain
    Our novel approach using backscatter observations is promising
      Can use more observations from all of domain
      No terrain complications: may be cheaper
    Further experiments required to determine
      how operators compare in operation (real SAR and topography)
      how many observations can we use?
      Thanks for listening!

## Slide 19: Positive nch bias

## Slide 20: Negative nch bias